## Slide 1: Modeling of Cable Suspension for the Carlina
Torben Andersen1
Mette Owner-Petersen1
Hervé Le Coroller2
1 Lund Observatory, Sweden
2 Observatoire de Haute Provence, France
Main skepticism: Can you keep the gondola
positioned sufficiently accurately? (Cable dynamics!!)

## Slide 2: Outline
Summary of 2011 study
Cable Model
Choice of design parameters

## Slide 3: Integrated Modeling
Telescope
Optics
Deformable
Mirrors
Telescope
Structure
Segmented Mirrors
Integrated Model
Segmented Mirror
Control
Segment
Actuators
Servo
Mechanisms
Reconstructor
Lenslet
Arrays
CCD
Established software infrastructure
Modelled Euro50
European ELT (E-ELT)
Thirty Meter Telescope (TMT)
Wrote Springer text book on integrated modeling
Used framework for Ubaye Carlina simulation 2011

## Slide 4: Carlina Study 2011
Anita Enmark ; Torben Andersen ; Mette Owner-Petersen ; Rijuparna Chakraborty and Antoine Labeyrie: "Integrated model of the Carlina Telescope“
Proc. SPIE 8336, Integrated Modeling of Complex Optomechanical Systems, 83360J (November 10, 2011)

## Slide 5: Carlina Study 2011 Model Structure
Ubaye Geometry
Generic study
Cables
Gondola
Winch
Controller
Wind
6 dof rigid-body motion
of Gondola
PSFs
etc
Gondola
forces
Optics Model

## Slide 6: Cable Suspension Submodel 2011
Re: A. Labeyrie

## Slide 7: Conclusions of Study
Ubaye concept may fulfill tolerances for short exposures
Difficult for long exposures:
  Two orders of magnitude in gondola position/tilt
More robust cable models and design parameter studies would be useful
Gondola position control approach important for project fundability

## Slide 8: Some Cable Applications

## Slide 9: Two Approaches Possible
Partial Differential Equations (PDE)
    Used for 2011 study
    Difficult to convert to first-order linear set of equations
Non-linear finite element model
    Make your own FE environment (Matlab)

## Slide 10: Non-Linear FE Model

## Slide 11: Modeling Approach
Set up geometrical and elastic stiffness matrices
Through iteration, determine ”exact” static form
For this operating point, determine eigenvectors and eigenfrequencies
Convert second-order model to first-order linear differential equations valid near operating point (2-300 states per cable)
Second-order model
First-order state-space
ABCD-model
(See paper for full equations)

## Slide 12: Strawman Example Similar to one Ubaye Cable
1.8 mm Kevlar 29
Mass 0.71 kg
Gravity
185.8 m
1344 N
0.121 m
Fracture stress 2923 Mpa (steel is ~2000 Mpa)
Preload stress 400 Mpa
E-modulus 70 Gpa (steel is 210 Gpa)
Density 1440 kg/m3 (steel is 7800 kg/m3)
Model with 40 elements
Taut wire regime: Deflection < 1/8 * chord length: Nearly parabolic
Slack wire regime: Deflection > 1/8 * chord length: Catenary

## Slide 13: Three Types of Eigenmodes Fixed End Supports
Eigenmode | Symmetry | Influence
In-plane | Symmetrical Anti-symmetrical | Important Little important
Out-of-plane | Symmetrical Anti-symmetrical | All unimportant
Axial | Symmetrical Anti-symmetrical | All important

## Slide 14: In-Plane Eigenmodes Strawman Example
Fixed end supports

## Slide 15: Eigenmode Summary Strawman Example
Number | Type | Symmetry | Eigenfrequency | Participation factor1
1 | out-of-plane | symmetrical | 1.59 | 0
2 | in-plane | symmetrical | 1.59 | 5.63
3 | in-plane | anti-symmetrical | 3.18 | 0.4
4 | out-of-plane | anti-symmetrical | 3.18 | 0
5 | out-of-plane | symmetrical | 4.76 | 0
6 | in-plane | symmetrical | 4.76 | 1.52
7 | in-plane | anti-symmetrical | 6.34 | 0.83
8 | out-of-plane | anti-symmetrical | 6.34 | 0
9 | out-of-plane | symmetrical | 7.90 | 0
10 | in-plane | symmetrical | 7.90 | 0.49
13 | in-plane | symmetrical | 11.0 | 0.09
17 | in-plane | symmetrical | 14.0 | 0.51
25 | axial | symmetrical | 18.9 | 5380
62 | axial | anti-symmetrical | 37.8 | 10700
81 | axial | symmetrical | 56.7 | 16000
82 | axial | anti-symmetrical | 75.4 | 21200
83 | axial | symmetrical | 94.1 | 26200
1 for a horizontal translation of end point
There is good agreement with analytical model and speed-of-sound model

## Slide 16: Model of Ubaye 3 m/s Wind
Sag exaggerated 5x

## Slide 17: Wind Effects
Wind on gondola
Wind on cable
Drag at 0.2-1 Hz
is critical
Flutter
(Vortex Shedding)
Excitation of
In-plane
eigenmodes
PSD
PSD
TF
100-600 Hz
Only an issue
near gondola
Eddy size
6-30 m for 0.2-1 Hz

## Slide 18: Winch on Ground or on Gondola?
Inherent dynamics are the same for the two cases; input is different

## Slide 19: Position Step at Left Cable End Strawman Example
Kevlar cable
Diam 1.85 mm
Chord 185.8 m
Gondola mass 50 kg
Cable mass 0.71 kg
Cable static stiffness 1024 N/m

## Slide 20: Position Step at Left Cable End Thicker Cable
Steel cable
Diam 4 mm
Chord 185.8 m
Gondola mass 50 kg
Cable mass 18.2 kg
Cable static stiffness 11105 N/m

## Slide 21: Winch on Ground or Gondola? Strawman Example with 50 kg Gondola
Input:
Winch on left end (blue)
Winch on gondola (red)
Output:
Gondola position
Conclusion:
Having winch on gondola is as bad as having it on ground

## Slide 22: Which Cable Diameter? Strawman Example
Cable diameter (mm) | Cable mass (kg) | Typical preload (N) | Crosswind force at 6 m/s (N) | Static stiffness along chord (N/m) | RMS Gondola excursion1 (mm)
1.85 | 0.72 | 1340 | 7.24 | 1020 | 21.8
3.70 | 2.88 | 5380 | 14.5 | 4100 | 2.50
5.55 | 6.47 | 12100 | 21.7 | 9200 | 0.72
7.60 | 11.5 | 33600 | 29.0 | 16400 | 0.31
1 Due to wind at 6 m/s acting on gondola,
and closed loop position control with winch
Conclusion:
Thicker cables are much better

## Slide 23: Is a Large Cable Preload Attractive? Strawman Example with cable diameter 5.4 mm
Cable preload (N) | Length of Unstressed cable (m) | Cable sag at Equilibrium (m) | Static Stiffness at end (N/m) | Lowest in-plane Cable eigen- frequency (Hz) | Lowest gondola eigenfrequency (Hz)
24200 | 183.195 | 0.601 | 9287 | 2.26 | 2.17
12100 | 184.488 | 0.121 | 9219 | 1.59 | 2.16
6056 | 185.142 | 0.243 | 9166 | 1.13 | 2.15
1363 | 185.668 | 1.081 | 7480 | 0.59 | 1.95
933 | 185.734 | 1.580 | 5380 | 0.57 | 1.65
361 | 186.000 | 4.088 | 698 | 0.55 | 0.59
Conclusion:
Above a certain limit, then the system is not very sensitive to preload

## Slide 24: Is a large E-Modulus Useful? Strawman Example, preload 1344 N
 | E=70 GPa | E=23.4 GPa | E=7 GPa
Cable eigenfrequency (mode 2) | 1.59 | 1.60 | 1.64
Cable eigenfrequency (mode 6) | 4.76 | 4.80 | 4.91
Cable eigenfrequency (mode 10) | 7.90 | 7.96 | 8.15
Cable eigenfrequency (mode 25) | 18.9 | 11.1 | 6.37
Cable eigenfrequency (mode 62) | 37.8 | 22.2 | 12.7
Static stiffness (N/m) | 1024 | 346 | 109
Sag (m) | 0.121 | 0.119 | 0.114
Lowest gondola eigenfrequency (Hz) | 0.72 | 0.42 | 0.24
Closed loop wind excursion of gondola, RMS (mm)1) | 18 | 63 | 196
1) with 50 kg gondola mass
Conclusion:
Take the highest E-modulus you can get

## Slide 25: Which Density?
Density (kg/m3) | 1440 | 7800
Preload (N) | 673 | 614
Sag (m) | 0.243 | 1.271
Lowest cable eigenfrequency (Hz) | 1.13 | 0.51
Static stiffness at end (N/m) | 1019 | 956
Lowest gondola eigenfrequency (Hz) | 0.72 | 0.71
Case 1: High preload
Density (kg/m3) | 1440 | 7800
Preload (N) | 40 | 174
Sag (m) | 0.851 | 5.09
Lowest cable eigenfrequency (Hz) | 0.55 | 0.49
Static stiffness at end (N/m) | 77.6 | 191
Lowest gondola eigenfrequency (Hz) | 0.49 | 0.31
Case 2: Low preload
Conclusion:
For reasonably high preloads, the density is not so important

## Slide 26: Which Material?
Material | Tensile strength (Mpa) | Density (kg/m3) | E-modulus (Gpa)
Polypropylene | 60 | 930 | 5
Polyester (Dacron) | 1150 | 910 | 15
Polyamid (Nylon) | 1000 | 1140 | 4
Aramid (Kevlar) | 3000-3500 | 1440 | 70-140
Steel | 1500-2000 | 7800 | 210
Stainless steel (Inox) | 500-1000 | 7850 | 200
Conclusion:
Aramid (Kevlar) or galvanized steel

## Slide 27: Conclusions
State-space simulation model ready
    Need a predesign
Kevlar or Steel
Take the largest cable diameter feasible
    5-7 mm at L~180-200 m
    Reduces influence of wind on gondola significantly
Use a reasonably high preload
    Axial elasticity should dominate over geometrical elasticity
    Reduces influence of cable dynamics and wind on cable
Wind load on gondola dominates over wind load on cable
Reaction wheels and masses seem necessary
    Detailed study advisable once the geometry is chosen

## Slide 29: Cable Modeling Challenge
Load carried through change of geometry
Usual finite element methods break down